# Adiabatic Circuits and Reversible Computing: 
Dispelling the Misconceptions
[first submitted complete draft]

[Editors: I am not bothering to hide my name because my identity will be obvious anyway to anyone in the field from the references, and I do not feel any desire to hide it.]

Michael P. Frank
CISE and ECE Departments
University of Florida
<mpf@cise.ufl.edu>

Abstract

The field of adiabatic circuit design, and its necessary relationship to reversible logic and reversible computing theory, is a topic that is quite rigorously grounded in firmly-established, fundamental physical and information-theoretic principles.  This subject is very clearly understood by all sufficiently well-educated parties.

However, for years, reversible computing has been subjected by a few confused skeptics to an awful riddling with numerous and egregious myths, misconceptions, confusions, and outright fallacies.  At present, the field sits by quietly, unfairly accused, widely misunderstood, and inadequately defended, and therefore, it remains largely ignored by the mainstream of low-power digital design researchers, despite its demonstrably vast (and inevitable!) long-term importance for the future of computing, which can be demonstrated using the most fundamental and certain laws of physics.

This unfortunate state of affairs is primarily the fault of nothing other than a lack of educational outreach effort on the part of us, the field’s proponents.  In this paper, I attempt to remedy that situation, by debunking some of the various myths and fallacies currently surrounding reversible computing, and in the process, revealing the true promise of the field.

## 1. Introduction

In this paper, we debunk the following frequently-promulgated myths and widely-committed fallacies of reasoning against adiabatic/reversible computing, as well as warning against some pitfalls in the design & analysis of adiabatic systems that are frequently encountered.

- Myth: Someone has proven that computing with less than order-kT free-energy loss per bit-operation is impossible.

- Myth: Physics isn’t reversible.

- Fallacy:  Since speed scales down in proportion to energy dissipation in adiabatic processes, adiabatic circuits can never be cost-efficient for high-performance computing.

- Fallacy: The failure of some skeptics to come up with efficient ways to physically implement adiabatic logic implies that it is impossible.

- Myth:  An energy-efficient adiabatic clock/power supply is impossible to build.

- Myth: Truly adiabatic physical operation can be achieved without  using reversible logic.

- Pitfall:  Using fundamentally non-adiabatic components (such as diodes) in the charge return path of an “adiabatic” circuit.

- Pitfall:  Forgetting to obey one of the fundamental adiabatic transistor rules that have been long known.

- Myth:  Sequential (as opposed to combinational) logic cannot be implemented adiabatically.

- Myth:  Adiabatic circuits inevitably require large numbers of clock/power rails and/or logic levels.

- Pitfall: Using the simplistic models of computing traditionally used in computational complexity theory to compare the efficiency of reversible vs. irreversible algorithms.

- Pitfall: Restricting oneself to using some overly restricted adiabatic logic family that does not offer the maximum possible asymptotic efficiency.

- Pitfall: Assuming that the most efficient reversible algorithm for a given computational task is similar to the most efficient irreversible algorithm for performing that task.

- Fallacy:  The algorithmic overheads of reversible computing outweigh the cost-efficiency benefits that can be gained from adiabatic operation.

- Myth:  Adiabatic design is necessarily difficult.

- Pitfall: Failing to optimize the extent to which reversible logic should be used in an adiabatic system.

- Pitfall:  Ignoring charge leakage in low-power/adiabatic design.

- Fallacy:  The fact that MOSFET on/off ratios get worse as devices get smaller means that leakage must eventually overwhelm bit-erasure losses, and so adiabatics is doomed.

- Fallacy: Smaller devices will always be better than larger devices.

- Fallacy: Simply saving the initial state and all inputs is enough to make a computation reversible.

- Fallacy:  The impossibility of ideal switches means that adiabatic switching circuits cannot implement reversible computing.

## 2. Background

First, let us start with some general background on the fundamental ideas behind adiabatic circuits and reversible computing.

As all of the top theoretical physicists are well aware, all of our best available, exhaustively-tested, standard models of fundamental physics plainly show that the dynamical behavior of our universe is completely reversible, or reverse-deterministic, meaning that any quantum state of the whole universe (along any spacelike “slice” through it) has a unique possible history looking backwards in time, as described in the Standard Model by the field-theoretic versions of Schrödinger’s equation.

As a consequence of this low-level reversibility (and determinism), the total amount of information of all types in the universe is exactly conserved.  In particular, information can never be destroyed.

As a direct consequence of this fact, whenever we purportedly “erase” 1 bit of known information in a computer, that information cannot really just vanish but instead merely becomes entropy (unknown information) which is expelled into the computer’s surroundings.  If the immediate environment is at temperature T, this increase in the environment’s entropy by 1 bit requires an accompanying increase in its heat content of 
T·(1 bit) = kT ln 2, by the very definition of temperature.  This waste heat represents a loss of free energy.

Even worse, in today’s computers, not just one, but rather, hundreds of thousands of bits’ worth of redundant physical information are used to encode each logical bit.  (Specifically, the relevant physical bits are the fermionic occupancy numbers, 0 or 1, of this many electron states per circuit node, which change occupancy when the node voltage changes, in today’s leading-edge VLSI technologies.)  All of this physical information is converted to entropy every time a bit is erased in today’s non-adiabatic circuits.

On the other hand, if a computer’s devices are designed to change state in a way that is logically reversible, in which no known bits are erased, then this argument does not apply, and, in principle, using a sufficiently clever adiabatic (nearly ballistic) mechanism, arbitrarily little entropy need be produced, and arbitrarily little free energy need be used up.  Of course, in practice, there are other sources of entropy generation such as leakage, frictional effects, and the finite quality factor Q of all real-world processes.  But, we know of no fundamental lower bounds that result from any of these sources that would require entropy generation per bit-operation to necessarily always be greater than k ln 2.

The very idea of adiabatic circuits rests squarely on this fundamental theoretical background.  Each circuit node contains a certain amount of known physical information, and an associated amount of free energy.  For voltage-encoded bits, as we all know, the associated free energy is ½ CV2 for circuit nodes of capacitance C subject to a logic voltage swing V. Normally, in, for example, static CMOS circuits, all of this physical information and therefore all of the associated energy gets lost whenever we change the logic level on the node.

However, if information about the state of the circuit node is available and is utilized when switching the state of node, then no information need be lost, and the switching can be done in such a way that most of the free energy is conserved in the circuit, and can be recycled for later reuse to store new results, rather than being dissipated to heat.

## 3. Myths, Fallacies, Pitfalls

In this section, we proceed to systematically debunk and explain each of the myths, fallacies and pitfalls about adiabatic switching and reversible computing that we enumerated in section 1.

1. Myth: Someone has proven that computing with less than order-kT (more precisely, kT ln 2) free-energy loss per bit-operation is fundamentally impossible, given the known laws of physics.

I have been digging into this subject intensely for the last 8 years, and I have never encountered a single logically valid (or even reasonably persuasive) argument in support of this claim.

It was John von Neumann who first conjectured this limit, in a 1949 lecture at the University of Illinois [], but he gave absolutely no proof of it.  Rolf Landauer at IBM attempted to justify von Neumann’s bound in 1961 [], but Landauer’s argument was only an informal one, and his particular line of attack was soundly refuted by Charlie Bennett (also of IBM) in 1973 [].  Mead and Conway also argued against this possibility in their widely-used VLSI textbook [], but again they gave no logically valid proof whatsoever, only a litany of specific examples of techniques that wouldn’t work.

In contrast, we do have many detailed theoretical models and constructions that strongly suggest that computing with arbitrarily little energy loss per operation really ought to be possible (in the limit of engineering improvements), so long as reversible logic is used.  These include classical-mechanical models by Bennett [],  Fredkin [], Drexler [], Merkle [], and Smith [], as well as quantum-mechanical models by Feynman [] and Margolus [].

Unfortunately for our educational efforts, each of the models that have been published so far suffers from some limitation or another.  Among the classical models, Bennett’s model was not time-efficient.  Fredkin’s contained chaotic instabilities.  Smith’s did not permit hardware reuse.  Furthermore, all of the mechanical approaches can be criticized as being impractical for not utilizing fast electronic signaling.

Among the quantum models, which  might yet be implemented electronically, Feynman’s only showed how to do serial computations, and Margolus’s model, although parallel, did not prove that active parallel processors could be successfully interconnected in a desirable 2D or 3D mesh architecture.  Also, both of these quantum models were somewhat abstract, and so, some people questioned whether they could ever be realized in detailed physical implementations.

Newer models of quantum computing [], although being necessarily internally reversible in their logic, do not really address the question of minimal energy dissipation at all, since all the quantum computing schemes described so far depend on external sources of timing signals, whose own dissipation is not modeled.

However, in the face of all of these various advances, the detractors of reversible computing have been forced to backpedal a bit, and to qualify and amend their statements, to make the more modest claim that sub-kT computing is, for some unstated reason, impossible only in any computation that does not suffer from one of the above-mentioned deficiencies or other.  Of course, there is never any real solid argument showing why repairing a given one of these deficiencies must necessarily always lead to dissipation, only conjecture.  And of course, each time a new model of reversible computing is devised that solves one more of the remaining deficiencies, the skeptics are forced to backpedal further.  They have no real valid arguments backing up their objections, nothing but a failure of imagination that is preventing them from exploring creative solutions to what is basically just an engineering problem, although admittedly a difficult one, but not one for which we have any real reason to expect it to be impossible to solve (such as, some fundamental law of physics being violated).

In fact, I believe that a combined, nano-electromechanical approach that combines the best features of several of the earlier-proposed reversible computing schemes can potentially work and moreover be highly practical in the long run for achieving sub-kT computing, and I am currently working on fleshing out and simulating such designs in detail.  If I had ever seen any valid argument showing me why sub-kT computing should really be impossible, then believe me, I would not be wasting my career on pursuing such efforts.  I have even tried proving the impossibility argument myself many times, in a variety of new ways, without any success.  Every time that I construct and analyze a more detailed and realistic physical model of computing (e.g., the one reported in []), which I try often, it still turns out to permit dissipation per bit-op that can be made arbitrarily small, given plausible projections of continuing engineering refinements.  I have never found any hard lower bound.

2. Myth: Physics isn’t reversible.

You sometimes will hear people (even some who claim to be physicists, but who don’t actually have a very clear understanding of modern physics) claim that, in contrast to what I said in section two, physics actually isn’t reversible, for one reason or another.  For the most part, these arguments simply betray the claimant’s misunderstanding of some aspect of physics or another.

First, some people cite the “arrow of time,” and wonder how the reversibility of microphysics can possibly be consistent with the apparent “one-way-ness” and irreversibility of macro-scale phenomena.  The answer is simply that so long as the initial state of the universe has a simple description, it is not surprising that even a reversible trajectory can result in states that become increasingly complex over time [].  The very same phenomenon has been experimentally observed to be ubiquitous even in trivially simple reversible cellular automaton models [].  To assume that microreversibility must imply time-reversal symmetry at the macro-scale is nothing other than an unjustified leap of logically invalid reasoning.

Next, other people complain that Liouville’s theorem from classical mechanics (which says that phase space volume is conserved) doesn’t necessarily imply reversibility; in fact, it’s easy to construct a simple artificial dynamics that conserves phase space volume, but is not reversible.  Although this is true, the correct argument for the reversibility of physics doesn’t actually rely on Liouville’s theorem itself, but rather on the more fundamental, quantum-mechanical principle of unitary time-evolution.

Still others remark that particle physicists have discovered that the property of exact time-reversal symmetry at the microscale appears to be violated.  Although this is true, in a strict technical sense (namely, in the sense that time-reversal symmetry still exists but apparently requires simultaneous charge and handedness reversals as well), this fact is totally irrelevant, because reversibility does not actually require time-reversal symmetry, specifically.  It only requires that the correct time-reversed version of the laws (whatever their form) remain deterministic, which is definitely the case in the well-tested Standard Model of particle physics, as well as in earlier, less refined quantum theories (and, even more generally, in all dynamical systems that admit a Hamiltonian description).

Still others claim, quantum mechanics is itself not really deterministic, i.e., not unitary, because of the manifest unpredictability of the results of measurements on quantum systems, and the superstitious concept of “wavefunction collapse” that is often invoked to explain this phenomenon.  These people are all looking at physics on the wrong level, at the perception of a subjective observer, rather than at the underlying reality. Today, the apparent nondeterminism of observed quantum phenomena has been soundly  established as merely being an emergent epiphenomenon that is completely implied by the more fundamental quantum laws (such as Schrödinger’s equation) that describe the unitary, fully deterministic and reversible evolution that really takes place in all quantum systems.

If you disagree with this statement, but you haven’t at least thoroughly read and understood Zurek’s papers on the subject, such as [], then please don’t pretend that you know anything about this issue yet.  In the opinion of myself and many others who have read his work, Zurek has convincingly demonstrated that apparent wavefunction “collapse” is nothing other than the natural, expected subjective appearance that results whenever the quantum state of a system becomes entangled (in a perfectly unitary fashion) with the state of a surrounding environment whose exact state is unknown.  In fact, some basic aspects of this process were explained as early as 1957 by Jaynes [].

3. Fallacy:  Since speed scales down in proportion to energy dissipation in adiabatic processes, adiabatic circuits can never be cost-efficient for high-performance computing.

The premise of this argument (that speed is proportional to energy dissipation in adiabatic processes) is true, for very fundamental reasons:  Namely, that as the speed of any given mechanism along a trajectory that carries out some process is increased, the mechanism’s kinetic energy also increases (quadratically), and given any constant decoherence rate for the quantum information contained in the motion, the kinetic energy decays with a constant mean-free-time, and this, in turn, implies that adiabatic losses increase proportionately to the process’s  quickness [].  The adiabatic theorem of quantum mechanics [] also confirms this relation.

However, the stated conclusion, that adiabatic logic can never be cost-effective for high-performance computing, does not logically follow from this premise, for two reasons.

First, there is no known lower limit to the constant of proportionality between a process’s quickness and its dissipation.  As engineering improvements reduce frictional coefficients and decoherence rates, and increase the state-insulation and quality factor Q of adiabatic logic mechanisms, the amount of energy dissipation of a reversible computation running at a given speed can apparently be reduced arbitrarily.  At least, if there is any lower limit, no one has succeeded in proving it yet.

Second, there are many solid reasons why, in the long run, most high-performance computing will be limited much more by power dissipation considerations than by the raw maximum speed of the individual logic devices.  Even though, in any given technology, adiabatic logic operations will always be slower than isolated non-adiabatic ones, this matters not. This is because of the fact that, due to their lower energy dissipation, more adiabatic devices can be packed together into an enclosure of given diameter without overheating, thereby reducing communication latencies for parallel computations.  So, together, the adiabatic devices can achieve a higher total rate of computation than the non-adiabatic devices, subject to the same heat flow constraints [,].  Even though a larger number of devices is needed, as the cost of manufacture of devices continues decreasing, as per Moore’s Law, larger numbers of devices can be afforded and used due to the power-performance improvements.  A recent and very detailed numerical analysis bears this out, and indicates that adiabatics could become thousands of times more cost-efficient than non-adiabatic technology for general-purpose computing by the middle of this century [13].

4. Fallacy: The failure of a few skeptics to come up with very efficient ways to physically implement adiabatic logic implies that this is impossible to do.

I discussed this fallacy already, after myth #1.  Reversible computing skeptics (e.g., []) often try to come up with a simple adiabatic logic mechanism and accompanying power supply off the top of their head, and the first combination they try doesn’t work well.  Naturally, such researchers consider themselves to be good engineers, and usually they probably are, but they mistakenly conclude that just because the specific method that they themselves tried didn’t work well, this means that the goal of efficient adiabatic circuits must be fundamentally impossible.  Often, writers (e.g., [4]) conclude that reversible computing must just be some sort of fantasy, somehow analogous to the long-debunked perpetual motion machine.

However there is a big difference between reversible computers, and perpetual-motion machines.  The endless attempts to build perpetual-motion machines always failed to work because of simple, fundamental principles of physics (whose very discovery was historically in fact inspired by those very same repeated failures), namely the conservation of energy, and the 2nd law of thermodynamics (entropy increases).

In contrast, reversible computing breaks no such laws, and is simply just one example of an adiabatic (nearly ballistic) process, of which we know many real, working physical examples.  With a carefully engineered mechanism, there is absolutely no reason why the ballistic motion of the system along a carefully-constrained trajectory cannot successfully carry out a computation with energy loss that is as small as we like.

If, on the other hand, it turned out that somehow there is some fundamental reason for an incompatibility between physics and efficient reversible computation, then this discovery would constitute a significant advancement in our understanding of the fundamental relationships between physics and computation, and thus it is worth pursuing, for that reason alone.  We are unlikely to make such discoveries if we do not at least make a thorough attempt to first eliminate all reasonable approaches, rather than abandoning the concept too quickly.

5. Myth:  An energy-efficient adiabatic clock/power supply is impossible to build.

This relates to the previous fallacy, in that a few engineers (e.g., [22]) have tried and failed to build one of these, and so they assume it must be impossible.  But we in the field have already long known (cf. []) that these simple schemes using MOSFET-switched inductors do not work well; in such circuits, the adiabatic losses scale down with the square root of quickness, rather than linearly.  But this single approach hardly scratches the surface of the whole world of engineering possibilities.

As mentioned earlier, I am currently working on some hybrid electromechanical approaches which I expect to perform much better.  The reason for this is that small mechanical oscillators (in vacuum) can have a very high Q, often thousands of times higher than the Q of, say, an electromagnetic inductor of comparable size.  (The underlying reason for this is that atoms are thousands of times more massive than electrons.)  This approach (if not many others as well) needs to be seriously attempted, before we can justifiably dismiss adiabatic logic as being forever impractical.

6. Myth: Truly adiabatic physical operation can be achieved without  using reversible logic.

Many authors have claimed to have accomplished this.  (I will avoid citing all their papers, to save them some embarrassment.)  Even without looking at the details of these papers, the ludicrousness of these claims can be anticipated by merely considering the absolutely fundamental nature of the connection between adiabaticity and reversibility in physics (see Myth #2).  Finding a way to achieve truly adiabatic operation without logical reversibility is tantamount to claiming to have overthrown all that we know about quantum mechanics, knowledge that has been confirmed by decades worth of physics experiments!  Any such claim (especially without experimental support) surely can only reflect some basic conceptual error or design mistake on the part of the claimant.

And, surely enough, whenever we examine the details of the claimed “dissipationless” mechanisms for logically irreversible operations, we always find that the claimant has made some serious error of understanding.

For example, some authors give the example of transforming a bit from the form of digital information to physical entropy and then back again, with no net increase in entropy.  This is fine, but any unknown bit of information (whether it is computationally accessible or not) is already entropy, by definition, and therefore its movement from one system to another need not imply any further entropy increase.  The correct statement of Landauer’s principle is only that the erasure of a known bit (one that is correlated with other bits in some definite way) necessarily creates entropy.  This is true almost by definition, as an immediate logical consequence of the fundamental unitarity of quantum mechanics.

Other authors try to propose erasing an n-bit register by reversibly decrementing the register until it is zero, then latching in the result (which is just a “single” irreversible operation) to provide empty space for later reuse.  But no, the fundamental laws of nature always have the last word.  It is easy to show that in order for the latch to work reliably for all order 2n steps, the energy dissipation from the one latching event must be at least as great as that required to erase all of the bits separately.

Or, if the zero state is not latched, but instead immediately continues along some further sequence of reversible interactions with the rest of the system, there is still order n entropy present in the exact timing of this event.  If the effect of the event is to have a predefined interaction with the rest of the computer, the entropy of this unknown timing information must still somehow be dealt with.

No, the only way to get rid of reversible logic, if there is one at all, must be at some higher level of programming, if, for example, we found a way to translate any irreversible computation into a reversible one taking exactly the same resources.  Then, a reversible low-level circuit could emulate an irreversible machine performing a given computation, and we could say that the emulated machine is not using reversible logic at its higher, software level (even though its emulator is still using it, at the hardware level).  But at present, no methods are known to do this in general, without introducing nontrivial (asymptotically increasing) overheads in the emulation process, and it furthermore seems likely that such overheads are unavoidable [].

7. Pitfall:  Using fundamentally non-adiabatic components (such as diodes) in a supposed “adiabatic” circuit.

Some researchers have attempted to design so-called “adiabatic” circuits that use components that are fundamentally non-adiabatic in their operation, such as diodes, in parts of a supposed adiabatic circuit, such as in the charge return path.  For very fundamental thermodynamic reasons, diodes are non-adiabatic: the asymmetry of their conductance in the two directions implies there must be a built-in voltage drop across them.  This “diode drop” is a source of significant non-adiabatic energy dissipation, dissipation that does not scale down as current decreases.  (The power dissipation scales down, but the total energy loss doesn’t.)  This is a basic error of adiabatic logic design; such circuit designs can never yield very significant energy savings.

8. Pitfall:  Forgetting to obey one of the fundamental adiabatic transistor rules that have been long known.

Watkins described one version of these rules as early as 1967 [].  These rules were previously long known in the electromechanical relay community as the rules for “dry switching.”  In that context, they were designed to prevent sparking between the relay contacts, which would cause corrosion and eventual failure.  The same rules are required to guarantee adiabatic operation internally within digital logic.

The rules are: (1) never turn on any conductance switch (e.g. a transistor) when there is a significant (non-negligible) voltage across it (i.e., between its source and drain terminals), and (2) similarly, never turn off any switch adiabatically when there is a significant current going through it.

The first rule is often recognized by adiabatic designers, but the second rule is just as often ignored.  The reason for this rule is that no real switch can proceed from the “on” state to its “off” state instantaneously; “threshold” voltages between on and off states are never true step functions.  There is always some gate voltage range and an accompanying transitional period, during which the switch has some intermediate level of conductance.  This transition period is particularly non-negligible when the switch’s state is itself being changed via a gradual, adiabatic transition, which is necessary in any fully-adiabatic logic.

During this transition, the initially negligible voltage drop across the device increases substantially, yet the resistance has still not grown extremely large, and so the P=V2/R power increases substantially during the transition, and the dissipation during the transition can easily overwhelm the dissipation in the rest of the circuit.  A simple numerical integration shows that a total dissipation much greater than kT results when performing adiabatic transitions at the very same speeds that would result in dissipation much less than kT in circuits that obey the rule [21].

Missing this second rule is an easy error to make.  Even my predecessors in the MIT reversible computing project made this mistake at one time; the original version of the SCRL circuit technique they designed [] actually contained this bug [21].  Fortunately, in the case of SCRL, the bug is easy to fix, by, for example, simply adding a single transistor to the 2-input NAND and NOR gate implementations [21].  Unfortunately, some other “adiabatic” logic schemes (e.g., de Vos’s circuits such as []) make this mistake more pervasively, and are less easy to repair.

One implication of rule (2) is that during the transitional period when a transistor is being turned off, the voltages on its source and drain nodes are either required to remain steady at (static or dynamic) fixed levels, or, if they are being varied, they must at least be independently varied (that is, without current flow through the transistor) along identical voltage trajectories.

9. Myth:  Sequential (as opposed to combinational) logic cannot be implemented adiabatically.

Some early adiabatic logic proposals (e.g., Hall’s []) did not offer a way to do sequential logic.  However, we now know that it is easy to do.  Of course, the function mapping the old state of the machine to its new state must be logically reversible, in order for the state-updating circuitry to be fully adiabatic.  But, any desired digital functionality can still be embedded in such a reversible design.  Fully reversible, general-purpose gate arrays [] and RISC-style microprocessors [] have been built.

10. Myth:  Adiabatic circuits inevitably require large numbers of clock/power rails and/or logic levels.

Although this was true of many early schemes, including MIT’s own SCRL [], more recently I have come up with a fully-adiabatic, pipelinable CMOS logic style (patent pending) that only requires 4 distinct clock/power input signals, and only uses 2 distinct voltage levels.

11. Pitfall: Using the simplistic models of computing that are traditionally used in computational complexity theory to compare the efficiency of reversible vs. irreversible algorithms.

The problem is that the traditional models of computing (studied by most theoretical computer scientists since Turing) are fatally inadequate for engineering purposes, because they completely ignore the unavoidable engineering realities that result from the reversibility of physics.  In the traditional models, reversible computations are a special case, a constrained restriction on the “more general” irreversible models.  As a result, reversible computing appears in those models to be fundamentally less efficient [24].  However, as a matter of fact, in physical reality, at bottom, the universe is always performing a reversible computation, and so to perform a computation using only “irreversible” logical operations is to place an extra, unnecessary restriction on the type of gates that are physically possible, that is, to constrain oneself to only using operations that necessarily transform some known information to entropy on each step.  The truly more general model of computation is one that permits reversible operations to be performed with negligible entropy generation whenever that is so desired by the logic designer or programmer.  It is a model that gives the designer strictly more power to optimize the efficiency of the computation.  And, in these new models, it is indeed possible to prove that reversible computing confers strictly greater asymptotic efficiency (by many measures, including time-efficiency and cost-efficiency) than any possible machine that is restricted to irreversible operations only [21].  As engineers, we need to focus our attention on these new models, which incorporate more of the relevant facts of known physics [].

12. Pitfall: Restricting oneself to using some overly restricted adiabatic logic family that does not offer the maximum possible asymptotic efficiency.

This is another trap that even our own group at MIT fell into, in limiting ourselves to our overly-tightly-constrained SCRL circuit style.  I realized that this was a mistake in the Spring of 2000, when I analyzed the asymptotic cost-efficiency of a simple ripple-carry adder in SCRL, taking the adiabatic speedenergy tradeoff into account, and realized that a strict SCRL approach was actually strictly less efficient asymptotically than a simpler, non-pipelined retractile cascade approach to doing ripple-carry adds.  Our group had made the mistake of assuming that just because pipelined circuits are nearly always more cost-efficient than non-pipelined circuits in the irreversible world, the same would be true in the reversible world.  But this is not so.

This example illustrates the more general point (pitfall #13) that the best reversible algorithm for performing a given task does not always have any direct correspondence to the best irreversible algorithm for performing that task.  Thus, designers must eventually be given direct access to reversible gates in the hardware, rather than being constrained to designing circuits in irreversible fashion and relying on design tools to make the translation.

However, in the short term, before reversible hardware algorithms have been designed for many problems, design tools that perform such translation may still have a useful role, namely in permitting legacy designs to be quickly reimplemented in a reversible style that obtains some of the benefits of adiabatic design.  In [13] I showed that even an automatic translation could achieve as much as a factor of 1,000( cost-efficiency boost (compared to irreversible circuits) by the 2050’s, although programmer input might yield as much as an additional factor of 100( improvement.

In light of this, I currently have several students working on a project to do synthesis of mostly-adiabatic circuits (with an optimized degree of reversibility) directly from VHDL source.  But in the longer run, we need to extend our hardware description languages themselves, to add reversible language constructs.

I have designed an adiabatic CMOS logic style that is, in a sense, just about the most general one possible, in that it permits implementing any 2-level or 3-level adiabatic CMOS circuit that is consistent with the fundamental adiabatic transistor rules that I described earlier.  I am currently working on developing an abstract language for describing hierarchical logic blocks in this circuit style that guarantees that so long as the declared timing constraints on the interfaces of two interconnected adiabatic logic blocks are simultaneously satisfied, the composition of the two logic blocks together is guaranteed to be adiabatic.  Design tools can automatically synthesize the most general description of the interface constraints for the adiabaticity of a higher-level block from those of its sub-blocks.  The lowest-level blocks, individual CMOS transistors, have simple descriptions in the constraint language.  Planned extensions to the VHDL language will allow programmers to describe efficient mostly-reversible hardware algorithms, from which efficient mostly-reversible adiabatic circuits can be easily synthesized.  Unfortunately, I cannot say more about these forthcoming developments at this time, as the University of Florida will be applying for a patent on the details.

13. Pitfall: Assuming that the most efficient reversible algorithm for a given computational task is similar to the most efficient irreversible algorithm for performing that task.

I already mentioned one counter-example in discussing ripple-carry ads in Pitfall #12.  Another example, mentioned in my thesis [21], is the all-pairs shortest-path problem in graph theory.  The Floyd-Warshall algorithm is a fairly effective irreversible algorithm, but its reversible equivalent is outperformed by an alternative reversible algorithm, which is less efficient in an irreversible setting.

As a result of the existence of this pitfall, we should not try to hide the underlying reversibility of physics from the (hardware or software) algorithm designer; otherwise we are tying their hands, and preventing them from creating the asymptotically most efficient algorithm for a given task.

14. Fallacy:  The algorithmic overheads of reversible computing outweigh the cost-efficiency benefits that can be gained from adiabatic operation.

The fact that algorithmic overheads (both constant-factor overheads, and overheads that asymptotically increase with problem complexity) do exist for reversible computing is true.  In terms of either the number of logical ops performed, or the algorithmic “spacetime” (bits in use, times cycles), reversible computing in general requires more computational work.  But, it is a fallacy to conclude that therefore reversible computing can not be more cost-efficient than irreversible computing overall.  As I mentioned in Pitfall #11 above, this conclusion results from using overly simplistic models of computing.  If using more physically realistic models, that take basic physical constraints from thermodynamics, quantum mechanics, and relativity into account, one sees that including the option for optimized mostly-reversible computation yields strictly greater cost-efficiency (even when all overheads are included) on many problems.  The reason is that real-world costs are determined not so much by algorithmic spacetime as by real spacetime (or, hardware times time), and not so much by ops performed as by free-energy spent.  When one studies the real costs, reversibility wins, hands-down [13].

15. Myth:  Adiabatic and/or reversible design is necessarily difficult.

Yes, it is somewhat difficult today, but this is primarily only due to a lack of suitable design tools.  As I describe in Pitfall #12 above, in my group, we are currently working on remedying that situation by designing HDLs and tools for synthesis of efficient circuits that are adiabatic and reversible to whatever degree the designer desires, and the technology is capable of.

Even with good tools, reversible design (of circuits or software algorithms) may still seem awkward at first, but I can attest from my own experience that one quickly becomes accustomed to it.  In cases where the designer is not yet comfortable with it, automated approaches can be used, although these will in general be less efficient than a hand-made reversible design (see pitfall #13).

16. Pitfall: Failing to optimize the extent to which reversible logic should be used in an adiabatic system.

It is a mistake of some reversible computing researchers to go too far, and claim that a computer should be completely reversible.  This is not good engineering.  Instead, the fraction of logic operations which are done reversibly should be optimized so as to maximize total cost-efficiency in the given VLSI technology and for the given application.  However, what is true is that our design methodology and tools should never artificially constrain the attainable degree of reversibility to be less than some arbitrarily chosen level.  Instead, good design practice should be capable of harnessing as great a degree of reversibility as may be beneficial in any future device technology.  As circuit Q’s increase, the optimal degree of reversibility increases as well [32].  Good forward-thinking design practice should make it possible to build designs that come as close to 100% reversible as the device characteristics may allow.

In my research reported in [13], I did exactly this: optimized the degree of reversibility of emulation algorithms so as to maximize system cost-efficiency, given the low-level device characteristics.  It is not particularly difficult.

Eventually, when/if device Q’s become high enough that fully-reversible operation of complete microprocessors becomes practical, we will even need reversible instruction-set architectures and programming languages, to enable the software designer to program hand-optimized reversible algorithms.  In anticipation of this event, work on such reversible architectures [30] and languages [21] has already begun.  However, for the near term, it is now clear that reversible HDLs will be more immediately valuable for energy-saving purposes, since they require less nearly perfect devices.

17. Pitfall:  Ignoring charge leakage in low-power/adiabatic design.

18. Fallacy:  The fact that MOSFET on/off ratios get worse as devices get smaller means that leakage will eventually set a permanent lower limit on energy dissipation, and therefore adiabatics is doomed.

19. Fallacy: Smaller devices will always be better.

I will treat all three of these items at once. Charge leakage, both across channels of nominally “off” transistors and along other pathways, is a major issue for all low-power electronics, including adiabatics.  It is a mistake to ignore it.

Furthermore, this problem becomes worse as circuits shrink, for the simple (and inevitable) reason that electron tunneling increases exponentially.  This increase can only be prevented by increasing the height of potential-energy barriers, but the combination of increasing potentials and decreasing distances is not compatible with keeping electric fields at a low enough level to prevent barrier materials from literally tearing themselves apart.

So, this problem will inevitably result in a stabilization of the minimum size of functional nanoelectronic circuits, at a pitch somewhere between 1 and 10 nm, sizes which are (not coincidentally) comparable to the Fermi wavelengths of electrons in conducting and semiconducting materials, respectively.

The question is whether the presence of substantial leakage at this limiting scale counts as a strike against the long-term economic viability of adiabatic circuits.  I claim that it does not.  My argument for this is simple.

First, even if device sizes level off, manufacturing costs per-device will arguably continue to decrease (even if gradually) over time, simply due to economic improvements in manufacturing process efficiency.  As the cost to build devices of a given size decreases, it becomes more cost-effective to actually build larger devices.  The larger devices, having larger separations, which in turn enable larger barrier voltages, will have leakage that is exponentially smaller.  As a result, at given cost, many more devices can be packed into a unit having given standby power consumption.  The total number of devices per system will continue to increase, while the leakage per device will decrease, meaning that an increasing fraction of logic operations would need to be done reversibly in a design that aims to maximize overall cost-efficiency.  It is easy to see that the required slight increases in device size (and the implied accompanying slight increases in inter-device communication delays) will be much more than compensated for by the presence of the larger number of devices having greater individual energy efficiency.  I am currently working on a detailed analysis to quantitatively illustrate these expectations.

20. Fallacy: Simply saving the initial state and all inputs is enough to make a computation reversible.

Many people make this mistake when they first hear that reversible computing involves a one-to-one function from old state to new state.  This is globally true for any deterministic computation in which the input is preserved.  But the bijectivity requirement for reversibility is actually stronger than this; it applies not just to the global state of the machine, but to the local state change that is performed in every single logic device (at least, to the extent to which the resulting degree of reversibility optimizes cost-efficiency).  Obviously, the mere remote presence of information that correlated with a given bit is not sufficient to reversibly uncompute that bit.  No, the correlated information has to be brought physically to the given bit and used to control its uncomputation.

21. Fallacy:  The impossibility of ideal switches means that adiabatic circuits cannot implement reversible computing.

This fallacy was committed by Schlaffer and Nossek in [].  After spending a long time showing that ideal voltage-controlled switches are thermodynamically impossible—which is already obvious—they bafflingly proceed, in a totally unjustified leap of illogic, to the conclusion that real-world, approximate, non-ideal switches are not useful for implementing physically reversible logic.  Of course, it is obvious that no real process can be perfectly physically reversible, meaning that it would have absolutely zero entropy generation, simply because no real system can ever be perfectly insulated from unwanted interactions with its uncontrolled external environment.  But, to the extent to which a real (e.g., CMOS) device can approximate an ideal device, for example by having high on/off current ratios, it can indeed implement circuits that are physically reversible, up to the limit determined by its imperfections.  This has been done, in all good adiabatic designs!

I hereby challenge Schlaffer and Nossek (or any other researchers) to demonstrate any factor apart from leakage and power supply Q (whose implications are already well understood) preventing the approach to physical reversibility of a logically reversible adiabatic circuit style that obeys all the transistor rules, such as, for example, SCRL, after it is repaired as I discussed in Pitfall #8 above, and in [21].

My suspicion is that Schlaffer and Nossek perhaps encountered one of the many “reversible” adiabatic logic schemes that didn’t actually obey the adiabatic transistor rules (e.g., [27]), and mistakenly concluded that just because that one example didn’t work, implementing asymptotically reversible logic (up to the leakage limit) correctly using adiabatic switching techniques was somehow impossible.  But, their paper does not at all prove this.

## Conclusion

After clearing up the many misunderstandings about the field of adiabatic circuits and reversible logic, it is clear that the subject is far from dead, and in fact, its ideas can be virtually proven to be a vital necessity for the long-term future of digital systems engineering.

# Footnotes

Computer industry giants, you would be well-advised to heed these words closely, for, I guarantee you, this technology is your destiny. (

However, it turns out that these are easy to fix.

This particular fix was suggested to me by Norm Margolus, one of my thesis advisors.

# Endnotes

Reported posthumously in John von Neumann, Theory of Self-Reproducing Automata, p. 66, University of Illinois Press, 1966.

Rolf Landauer, “Irreversibility and heat generation in the computing process,” IBM Journal of Research and Development, 5:183-191, 1961.  http://www.research.ibm.com/journal/rd/441/landauerii.pdf.

Charles H. Bennett, “Logical reversibility of computation,” IBM J. of Res. & Dev., 17(6):525-532, 1973.  http://www.aeiveos.com/~bradbury/Authors/Computing/Bennett-CH/LRoC.html.

Carver Mead and Lynn Conway, Introduction to VLSI Systems, Addison-Wesley, 1980.

C. H. Bennett, “The Thermodynamics of Computation—a Review,” International Journal of Theoretical Physics, 21(12):905-940, 1982.

Edward F. Fredkin and Tommaso Toffoli, “Conservative Logic,” Int’l. J. of Theor. Phys., 21(3&4):219-253, 1982.

K. Eric Drexler, Nanosystems: Molecular Machinery, Manufacturing, and Computation, John Wiley & Sons, Inc., 1992.  http://www.zyvex.com/nanotech/nanosystems.html.

Ralph C. Merkle, “Two types of mechanical reversible logic,” Nanotechnology, 4:114-131, 1993.

Warren D. Smith, “Classical reversible computation with zero Lyapunov exponent,” NECI Technical Report, Feb. 25, 1999,  http://www.neci.nec.com/homepages/wds/pu-fred-lyap.ps.

Richard Feynman, “Quantum mechanical computers,” Int’l. J. Theor. Phys., 21(6&7):467-488, 1982.

Norman H. Margolus, “Parallel Quantum Computation,” in Complexity, Entropy, and the Physics of Information, Wojciech Zurek, ed., 1990.

Michael A. Nielsen and Isaac L. Chuang, Quantum Computation and Quantum Information, Cambridge University Press,  2000.

Michael P. Frank, “Nanocomputer Systems Engineering,” in the proceedings of the 2003 Nanotechnology Conference & Trade Show, San Francisco, Feb. 2003, Nano Science & Technology Institute, 2003.  http://www.cise.ufl.edu/research/revcomp/theory/NanoTech2003/Frank-NanoTech-2003.ps.

Richard Feynman, “The Distinction of Past and Future,” ch. 5 of The Character of Physical Law, MIT Press, Mar. 1967.

N. H. Margolus, Physics and Computation, Ph.D. thesis, Massachusetts Institute of Technology, Dept. of Physics, 1988.

Wojciech H. Zurek, “Decoherence, einselection, and the quantum origins of the classical,” preprint http://arxiv.org/abs/quant-ph/0105127, July, 2002.

E. T. Jaynes, “Information Theory and Statistical Mechanics. II”, The Physical Review, 108(2):171-190, Oct. 15, 1957.

Michael P. Frank, “The Adiabatic Principle: A Generalized Derivation”, UF Reversible Computing Project Memo #M14, Aug. 2001, http://www.cise.ufl.edu/research/revcomp/memos/M14_adiaprinc.ps.

David J. Griffiths, Introduction to Quantum Mechanics, Prentice Hall, 1995.

M. P. Frank and Thomas F. Knight, Jr., “Ultimate Theoretical Models of Nanocomputers,” Nanotechnology, 9(3):162-176, 1998.  Presented at the Fifth Foresight Conference on Molecular Nanotechnology, Palo Alto, CA, Nov. 1997.  http://www.cise.ufl.edu/~mpf/Nano97/abstract.html.

M. P. Frank, “Reversibility for Efficient Computing,” Ph.D. Thesis, MIT, Dept. of EECS, June 1999. http://www.cise.ufl.edu/~mpf/thesis/phdthesis.html. Slightly revised and expanded version at http://www.cise.ufl.edu/~mpf/manuscript.

Thomas Indermaur and Mark Horowitz, “Evaluation of Charge Recovery Circuits and Adiabatic Switching for Low Power CMOS Design,”

Lars Svensson, “Adiabatic switching,” in Anantha P. Chandrakasan and Robert W. Broderson, Low Power Digital CMOS Design, ch. 6, pp. 181-218, Kluwer Academic Publishers, 1995.

M. P. Frank and M. J. Ammer, “Relativized Separation of Reversible and Irreversible Space-Time Complexity Classes,” submitted to Information and Computation, May 2001.  Currently under revision.  http://www.cise.ufl.edu/~mpf/rc/memos/M06_oracle.html.

Boyd G. Watkins, “A low-power multiphase circuit technique,” IEEE Journal of Solid-State Circuits, pp. 213-220, Dec. 1967.

S. G. Younis and T. F. Knight, Jr., “Asymptotically Zero Energy Split-Level Charge Recovery Logic,” in International Workshop on Low Power Design, pp. 177-182, 1994.

Alexis de Vos, “A 12-transistor c-MOS building-block for reversible computers,” Int. J. Electronics, 1995, 79(2):171-182.

J. Storrs Hall, “An electroid switching model for reversible computer architectures,” in PhysComp ’92: Proceedings of the Workshop on Physics and Computation, October 2-4, 1992, Dallas, Texas, pp. 237-247, IEEE Computer Society Press, 1992.

M. P. Frank, Carlin Vieri, M. Josephine Ammer, Nicole Love, Norman H. Margolus, and Thomas F. Knight, Jr., “A scalable reversible computer in silicon,” in Calude et al., Unconventional Models of Computation, pp. 183-200, Springer, 1998. http://www.cise.ufl.edu/~mpf/rc/flattop/ft.html.

Carlin J. Vieri, Reversible Computer Engineering and Architecture, Ph.D. thesis, MIT, Dept. of EECS, 1999.

Saed G. Younis, Asymptotically Zero Energy Computing Using Split-Level Charge Recovery Logic, Ph.D. thesis, MIT EECS dept., 1994.

Michael P. Frank, “Nanocomputers—Theoretical Models,” invited review chapter to appear in Hari Singh Nalwa, ed., Encyclopedia of Nanoscience and Nanotechnology, American Scientific Publishers, 2003.   http://www.cise.ufl.edu/research/revcomp/Nanocomputers.doc.

A. Schlaffer and J. A. Nossek, “Is there a connection between adiabatic switching and reversible computing?”, Institute for Network Theory and Circuit Design, Munich University of Technology, 1997, http://citeseer.nj.nec.com/schlaffer97is.html.